## Slide 1
William Stallings Computer Organization and Architecture 8th Edition
Chapter 3
Top Level View of Computer Function
and Interconnection
Book by : Computer, Architecture and Organizations, 8th Edition ,William Stalling
Original Slides by : Adrian J Pullin

## Slide 2
Top Level View of Computer
Function and Interconnection

## Slide 3: Lecture Outcomes
Understanding of:
Computer Components
Computer Function
Instruction Fetch and Execute
Interrupts

## Slide 4: Program Concept
Hardwired systems are inflexible
General purpose hardware can do different tasks, given correct control signals
Instead of re-wiring, supply a new set of control signals

## Slide 5: What is a program?
A sequence of steps
For each step, an arithmetic or logical operation is done
For each operation, a different set of control signals is needed

## Slide 6: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals
We have a computer!

## Slide 7: Components
The Control Unit and the Arithmetic and Logic Unit constitute the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory

## Slide 8: Computer Components : Top Level View

## Slide 9: Instruction Cycle
Two steps:
  Fetch
  Execute

## Slide 10: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 11: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 12: Example of Program Execution

## Slide 13: Instruction Cycle State Diagram

## Slide 14: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 15: Program Flow Control

## Slide 16: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 17: Transfer of Control via Interrupts

## Slide 18: Instruction Cycle with Interrupts

## Slide 19: Program Timing Short I/O Wait

## Slide 20: Program Timing Long I/O Wait

## Slide 21: Instruction Cycle (with Interrupts) - State Diagram

## Slide 22: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt

## Slide 23: Multiple Interrupts - Sequential

## Slide 24: Multiple Interrupts – Nested

## Slide 25: Review Questions
What general categories of functions are specified by computer instructions?
List and briefly define the possible states that define an instruction execution.
List and briefly define two approaches to dealing with multiple interrupts.

## Slide 26
Thank you