## Slide 1
William Stallings Computer Organization and Architecture 8th Edition
Chapter 3
Cont. Top Level View of Computer Function
and Interconnection
Book by : Computer, Architecture and Organizations, 8th Edition ,William Stalling
Original Slides by : Adrian J Pullin

## Slide 2
Top Level View of Computer
Function and Interconnection

## Slide 3: Lecture Outcomes
Understanding of:
Time Sequence
Computer Modules
Computer Interconnection
Bus Structure
Bus Arbitration
PCI

## Slide 4: Time Sequence of Multiple Interrupts

## Slide 5: Connecting
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU

## Slide 6: Computer Modules

## Slide 7: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing

## Slide 8: Input / Output Connection(1)
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 9: Input/Output Connection(2)
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)

## Slide 10: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 11: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)

## Slide 12: What is a Bus?
A communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Power lines may not be shown

## Slide 13: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit

## Slide 14: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 15: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals

## Slide 16: Bus Interconnection Scheme

## Slide 17: Big and Yellow?
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires

## Slide 18: Physical Realization of Bus Architecture

## Slide 19: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that co-ordination of bus use can adversely affect performance
    If aggregate data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems

## Slide 20: Traditional (ISA) (with cache)

## Slide 21: High Performance Bus

## Slide 22: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance

## Slide 23: Bus Arbitration
More than one module controlling the bus
e.g. CPU and DMA controller
Only one module may control bus at one time
Arbitration may be centralised or distributed

## Slide 24: Centralised or Distributed Arbitration
Centralised
  Single hardware device controlling bus access
    Bus Controller
    Arbiter
  May be part of CPU or separate
Distributed
  Each module may claim the bus
  Control logic on all modules

## Slide 25: PCI Bus
Peripheral Component Interconnection
Intel released to public domain
32 or 64 bit
50 lines

## Slide 26: PCI Bus Lines (required)
Systems lines
  Including clock and reset
Address & Data
  32 time mux lines for address/data
  Interrupt & validate lines
Interface Control
Arbitration
  Not shared
  Direct connection to PCI bus arbiter
Error lines

## Slide 27: PCI Bus Lines (Optional)
Interrupt lines
  Not shared
Cache support
64-bit Bus Extension
  Additional 32 lines
  Time multiplexed
  2 lines to enable devices to agree to use 64-bit transfer
JTAG/Boundary Scan
  For testing procedures

## Slide 28: PCI Commands
Transaction between initiator (master) and target
Master claims bus
Determine type of transaction
  e.g. I/O read/write
Address phase
One or more data phases

## Slide 29: PCI Read Timing Diagram

## Slide 30: PCI Bus Arbitration

## Slide 31: Review Questions
What is the benefit of using a multiple-bus architecture compared to a single-bus architecture?
List and briefly define the functional groups of signal lines for PCI.

## Slide 32
Thank you