## Slide 1
William Stallings Computer Organization and Architecture 8th Edition
Chapter 9
Cont. Computer Arithmetic
Book by : Computer, Architecture and Organizations, 8th Edition ,William Stalling
Original Slides by : Adrian J Pullin

## Slide 2
Cont. Computer Arithmetic
Book by : Computer, Architecture and Organizations, 8th Edition ,William Stalling
Original Slides by : Adrian J Pullin
Adapted by: Ilyas Younus Essani

## Slide 3: Lecture Outcomes
Understanding of:
Division
Division Unsigned Binary Integer
Booth’s Algorithm for Division
Floating Point
Floating Point Addition & Subtraction
Floating Point Multiplication & Division

## Slide 4: Division
More complex than multiplication
Negative numbers are really bad!
Based on long division

## Slide 5: Division of Unsigned Binary Integers
001111
1011
00001101
10010011
1011
001110
1011
1011
100
Quotient
Dividend
Remainder
Partial
Remainders
Divisor

## Slide 6: Flowchart for Unsigned Binary Division

## Slide 10: Floating Point
+/- .significand x 2exponent
Misnomer
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)

## Slide 11: Floating Point Examples

## Slide 12: Signs for Floating Point
Mantissa is stored in 2s compliment
Exponent is in excess or biased notation
  e.g. Excess (bias) 128 means
  8 bit exponent field
  Pure value range 0-255
  Subtract 128 to get correct value
  Range -128 to +127

## Slide 13: Normalization
FP numbers are usually normalized
i.e. exponent is adjusted so that leading bit (MSB) of mantissa is 1
Since it is always 1 there is no need to store it
(c.f. Scientific notation where numbers are normalized to give a single digit before the decimal point
e.g. 3.123 x 103)

## Slide 14: FP Ranges
For a 32 bit number
  8 bit exponent
  +/- 2256  1.5 x 1077
Accuracy
  The effect of changing lsb of mantissa
  23 bit mantissa 2-23  1.2 x 10-7
  About 6 decimal places

## Slide 15: Expressible Numbers

## Slide 16: Density of Floating Point Numbers

## Slide 17: IEEE 754
Standard for floating point storage
32 and 64 bit standards
8 and 11 bit exponent respectively
Extended formats (both mantissa and exponent) for intermediate results

## Slide 18: IEEE 754 Formats

## Slide 19: FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 20: FP Addition & Subtraction Flowchart

## Slide 21: FP Arithmetic x/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage

## Slide 22: Floating Point Multiplication

## Slide 23: Floating Point Division

## Slide 24: Review Questions
What are the differences among positive overflow, exponent overflow and significant overflow?
What are the basic elements of floating-point addition and subtraction?
Give a reason for the use of guard bits.
List four alternative methods of rounding the result of a floating-point
operation.

## Slide 25
Thank you